## Slide 1: RSpec 0.1 - Vehicle Counter
Webcam window (parameter: x by y in pixels)
Configurable region of interest (ROI)
  increases focus and reduces processing load
Configurable counting position (cntPos)
Vehicles represented by bounding box
  must be associated with track in order to
Tracking process
  new motion detection in new frame
  associate with existing track or create new track (trackID)
  if track above configurable confidence level, make track visible as vehicle (vehicle ID)
  if track fallls below confidence level, delete track
Counting process
  if vehicle passes count position, increase counter, mark vehicle as counted
ToDo [2017-10-14]
  centralized parameter struct in scene: framesize (x,y), confidence, samevelocity, blobArea(min,max)...videosize
  calculate all positions, velocities relative to window size
ROI
cntPos

## Slide 2: Modules
  Config
  all configuration data used in other classes
  loaded from Sqlite database
      on startup
      on request
    classes: config, parameter
  SceneTracker
  ctor: ptr to config
  read config
      in ctor
      on parameter change
  Observer pattern (notify on change, pull data)
  instantiate:
    1. instantiate config (subject)
    2. instantiate scene (observer)
    3. call config::attachObserver(pScene)
  FrameHandler
  ROI
  Segmentation
  Visualization (graphical + textual overlays)
blobs
vehicles
pull
pull
    on parameter change
    on parameter change
  Recorder
  ctor: ptr to config
  read config
      in ctor
      on parameter change
count record
Observer pattern

## Slide 3: Config
State machine
  init std parameters
  read cmd line options
  read config file / sqlite db
Cmd line options:
  i(nput)
    <0> video device (if empty, take standard cam)
    "input file": file to read from
  w(orking directory)
    "working path" below home
  o(utput file)
    "file name": file to write to
    roi_blobs
  r(ate)
    <fps> frames per second for video device
  v(ideo size)
    <320x240> frame size
  if the same option occurs more than once, the first option (and opt arg) is taken
path: look for "input file" in
  current directory
  /home
  /home/working path

## Slide 4: Config - Test Cases
program_options
  no options
  not specified options  are not considered
  opt arguments
config
  check /home
  create config file (sqlite)
  store and retrieve data

## Slide 5: FrameHandling
Data
  capSource (isFromFile, fileName, deviceName)
  framesize
  region of interest (ROI)
  frame
  roi_blobs
Functions
  applyROI
  segmentFrame
  findBlobs
  showFrame

## Slide 6: Object Tracking (Assign Blobs to Tracks)
tracking.h object model
New blobs represented by
TrackEntry
Rect bbox
Point centroid
double distance
Point2d velocity
Track
vector<TrackEntry> history
int id
int confidence
int idxCombine
bool markedForDelete
Point2d avgVelocity
bbox
centroid
Track::Update(list<TrackEntry>& blobs)
  Assign blobs to Track based on
    similarity
    sort existing blobs by proximity, assign closest
  new blob assigned: increase confidence
  no blob assigned: calculate substitute value for blob, decrease confidence
  confidence <= 0  mark for delete, unassign ID
Track::AddTrackEntry(TrackEntry&)
  include Update velocity in AddTrackEntry, not as separate fcn
Track::AddSubstitute()
  velocity remains unchanged

## Slide 7: Tracker - Test Cases
class TrackEntry
  centroid calculation
  hasSimilarSize
class Track
  velocity calculation
  substitute track entry
  updateTrack
    take closest
    take similar
  delete track, if confidence drops below zero
class SceneTracker
  allow for max 10 Tracks (Track-ID)
  updateTracks
    max 10 Tracks
    delete orphaned
    update new

## Slide 8: Tracker - Parameters
SceneTracker
  track_max_confidence: max. confidence of tracks allowed (6)
  track_max_deviation: max. deviation in length and height (80%)
  track_max_dist: max. distance in pixels between centroids (30)
  max_n_of_tracks: max. number of tracks per scene (9)
  count_confidence: min. confidence for counting vehicles (3)
  count_pos_x: horizontal counting position in pixels (90)
  count_track_length: min. length of track for counting vehicles (20)
  truck_width_min: min. truck width in pixels (60)
  truck_height_min: min. truck height in pixels (28)

## Slide 9: Vehicle and Track representation in scene
Scene
list<Vehicle> vehicles
list<Tracks> tracks
Rect TrackingWindow const int confCreate = 3
const int confDelete = 1
Vehicle
Rect bbox
list<Track*> pTracks
Point2d velocity
const int confAssign = 3
const int confVisible = 4
Scene::UpdateTracks(list<TrackEntry>& blobs)
  for each track in szene:
    Track::Update (updates existing tracks from blobs)
    DeleteTracks, ReturnID if confidence drops to zero (IsMarkedForDelete == true)
  for each unassigned blob in blobs
    CreateTrack, assign ID
Scene::UpdateVehicles(std::list<Track>& tracks)
Scene::CreateVehicles
  for each track: !IsAssigned && (confidence > Scene::confCreate) && IsEntering  add new Vehicle(Track&)
Scene::DeleteVehicle
  for each vehicle
    confidence of all assigned tracks low  UnassignTrack by erasing related tracks element
Scene::CombineTracks
  execute in each update step:
  combine tracks that are close to each other and have similar velocity
  combined tracks have same idxCombine
Track

## Slide 10: CreateVehicleFromTracks
Create vector of pTracks, that need to be combined (similar velocity, close to each other)
  INPUT: list of pTrack  pTracks
  OUTPUT: vector of lists of pTrack  vCombTracks
move pTrack to vCombTrack[idx] as last element
++pTrIterator points to next element
idx = 0; pTrIterator = pTracks.begin()
vCombTrack last element and pTrack element are close & have similar velocity?
yes
no
pTrIterator != end?
pTrIterator != end?
move pTrack to vCombTrack[idx] as last element
++pTrIterator points to next element
++pTrIterator
++idx
pTrIterator = pTracks.begin() // start with remaining elements in pTracks again
For all combined tracks
  add bboxes (logical or)
  average velocity
  create vector of contour indices

## Slide 11: CreateVehiclesFromTracks - Timing
Tr1
1
vCombTracks
[0]
[0]
Tr2
Tr3
Tr1
Tr2
Tr3
Tr2
Tr3
Tr3
itTr
itTr
itTr
[0]
Tr1
[1]
[0]
Tr2
Tr1
Tr2
Tr1
++idx
Time Steps
2
3
4
5
[1]
[0]
Tr3
itTr = pTracks.begin()
pTracks

## Slide 12: Vehicle Segmentation Preconditions
Vehicles consist of a combination of tracks, that is re-calculated at each update step
Vehicle::Update(std::list<Track>&)
  clear pTracks (newly created at each update step )
  for each track in scene: !IsAssigned && (confidence > Scene::confCreate)
    HasSameVelocity, IsClose, IsEntering?  add track(*tr) to vehicle, set assigned bit
    set assigned bit for
    confidence to assign > confidence to un-assign (see ValidateTracks)
  Update OutboundRect
  UpdateVelocity (see next page)
IsEnteringScene
IsEntering
IsLeaving
TrackingWindow
CountingLine
Vehicle
Rect bbox
list<Track*> pTracks
Point2d velocity
const int confVisible = 4

## Slide 13: Vehicle Segmentation from Tracks
For each Track:
  HasSimilarVelocity
  IsClose
  IsEntering
   AddTrack
UpdateOutboundRect
UpdateVelocity
  Average velocity of associated tracks
ToDo:
  idxContour not valid for substitute values of track entry:
    // ToDo: creating a fgMask from contours fails, if substitute values for blobs were calculated (conf < maxConf)
    // in this case track entry must not assigned to idxContour
  vehicle must go over entire scene (and are only counted in this case)
  substitute value for vehicle, if
    track is lost
    vehicle is obscured
Outbound rectangle for vehicle representation
Test scenarios
  check IsClose
  check HasSimilarVelocity
  combination of tracks (depending on position and velocity)
  calculation of outbound rectangle
  calculation of velocity
  Vehicle::Update: assignment of tracks

## Slide 14: Testscenario
Vehicle::IsClose(track&)
  dist = 30
  vehicle(0, 0, 100, 50)
  track1(120, 0, 100, 20)  IsClose == true
  track2(150, 150, 100, 100)  IsClose == false
vehicle.bbox
track1
track2
dx < dist
dx > dist

## Slide 15: ToDo Object Tracking
Combine tracks
  combine tracks, depending on same velocity
  use only tracks with high confidence
Counting
  count only
Refactoring
  make all class variables private
  implement Blob ID handling as Track method (static list for track IDs)
  Tracks::DeleteTrack
Set Up Test Environment
  tests for tracking classes (in tst_track)

## Slide 16: Backup

## Slide 17: Motion based multiple object tracking with stationary camera
Initialize tracks
Read video frame
Detecting moving objects in each frame, using background subtraction
  Background mdeling
  Background initializaiton
  Background maintenance
  Foreground detection
Associating the detections corresponding to the same object over time
  Assign detections to track
  Update assigned tracks
  Update unassigned tracks
  Delete lost tracks
  Create new tracks
    Assumption: each newly detected object starts a new track (judged by size and location)
Display tracking results
Motion detection
Object tracking

## Slide 18: Read video frame: Test
Single step mode for reading and displaying frames  done
Continuous mode, based on timer (100 ms / frame)  done
Reference videos  done (c#\recordings\2015-03-30_Überschneidung_V2.wmv – 1:20 min)
Comparison of different background modeling algorithms (Aforge simple background modeling, CV MOG, CV MOG2)  done, MOG2 is best
Apply filters to improve results (e.g. busses contain of multiple blobs, as windows are not recognized as foreground)
Filter sequence: blur, MOG, erosion, combine blobs
Testinfrastructure, to compare results

## Slide 19: Detecting moving objects in each frame: Test
Display background and foreground mask in seprarate window
Show bounding box and centroid of each identified blob in original and mask window
Control panel for parametrization
Background
Original frame
Foreground mask
Control panel

## Slide 20: Detecting moving objects in each frame: Test control panel
Control panel functionality
Run
Pause
Single Frame
Go to Frame: